## Slide 1: Software Debug and Control
Kevin Weldon
January 2022
Notes: Two example designs created to show how to interface with Intel FPGAs (CSR) using software. Tcl and C

## Slide 2: Goals
To demonstrate a platform which can be used to set control registers and read/respond to status (CSR) registers
Gain familiarity with Platform Designer as a tool to quickly design address mapped interfaces
Lean the basics of Intel’s Tcl API
Design simple Nios V design to demonstrate CSR access
Understand the Nios V tool flow
Obtain complete working example designs of both the Tcl and C flows

## Slide 3: Tool Utilized in Example Designs
Platform Design
  System integration tool used to automatically generate interconnect logic connect IP and subsystems
Nios V
  Next generation soft processor based on the open-source RISC-V Instruction Set
JTAG to Avalon Bridge
  IP core providing a connection between host systems (desktop computer) and an Avalon Interface based Platform Designer System
Avalon Interface
  Defines a memory mapped and stream interface standard to communicate between IP blocks in Platform Designer

## Slide 4: Documentation / Instructions
JTAG_Read_Write_Example_Guide_Tcl.doc
NiosV_Read_Write_Example_Guide_C.doc

## Slide 5: Debug and Control Using TCL

## Slide 6: Platform Designer System – JTAG to Avalon Bridge

## Slide 7: Platform Designer System – Block View
clk
reset
clock_in
reset_in
JTAG
master
ram_32bit
pio_8bit
Avalon
Memory Mapped
Interface
pio_8bit
JTAG Connection from host PC

## Slide 8: Top Level System – Block View
clk
issp_reset
Platform Designer
System
led
reset
JTAG Connection from host PC

## Slide 9: Reset Control Using Tcl
toggle_issp.tcl script is used to toggle the reset register
  The script makes a connection to the FPGA through JTAG
  The In System Sources and Probes (ISSP) register instantiated in the design is then toggled, providing a reset to the system
    start_insystem_source_probe -hardware_name $hardware2use -device_name $device
    write_source_data -instance_index $ISSP_INDEX -value "1"
    after $RESET_MS
    write_source_data -instance_index $ISSP_INDEX -value "0"
    end_insystem_source_probe

## Slide 10: Debug & Control Tcl Script
The read_write_example.tcl script is used to interface with the FPGA.
Notes: Global variables are used here to more closely match the structure of the equivalent C-code.

## Slide 11: Example Project Contents
Filename | Description
cleanup.bat | Removes all restored and generated files.
compile_design.bat | Compiles the FPGA from a Windows Prompt.
NiosV_Read_Write_Example_Guilde.pdf | Description and instructions for the example design.
open_cmd_prompt.bat | Opens a Windows Command Prompt in the present working directory.
path_env_check.bat | Windows batch file to help check correctness of PATH environment variable.
program_fpga.bat | Windows batch file script to run the program_fpga.tcl and toggle_issp.tcl scripts from a Windows Prompt.
program_fpga.tcl | Tcl script to assist in the programming of the FPGA.
read_write_example.tcl | Software application file written in tcl.
restore_qar.bat | Windows batch file script to restore the Quartus project from the Quartus archive (.qar file)
run_app.bat | Windows batch file script to run the read_write_example.tcl application.
toggle_issp.tcl | Tcl script to toggle the internal reset register using In System Sources and Probes (ISSP).
top_21_4_0_67.qar | Quartus project archive file, including Platform Designer system and Verilog files.

## Slide 12: Demo

## Slide 13: Debug and Control Using C

## Slide 14: Platform Designer System – JTAG to Avalon Bridge

## Slide 15: Platform Designer System – Block View
clk
reset
JTAG
UART
reset_in
Nios V
ram_32bit
pio_8bit
Avalon
Memory Mapped
Interface
pio_8bit
Data_instruction_ram
JTAG Connection from host PC
clock_in

## Slide 16: Top Level System – Block View
clk
issp_reset
Platform Designer
System
led
reset
JTAG Connection from host PC

## Slide 17: Block Diagram Comparison

## Slide 18: Debug & Control C Program
The read_write_example.c program is used to interface with the rest of the FPGA
IOWR_32DIRECT(RAM_32BIT_BASE, 0, 0x01234567);
The above command is similar to the following C instruction:
*(uint32_t*)(RAM_32BIT_BASE) = 0x01234567;
And is équivalent to the following Tcl API command:
master_write_32 $jm $RAM_32BIT_BASE 0x01234567

## Slide 19: Code comparison

## Slide 20: Example Project Contents
Filename | Description
Makefile | Makefile to build and manage FPGA and software application projects.
NiosV_Read_Write_Example_Guilde.pdf | This document.
open_cmd_prompt.bat | Opens a Windows Command Prompt in the present working directory.
path_env_check.bat | Window batch file to help check correctness of PATH environment variable.
program_fpga.tcl | Tcl script to assist in the programming of the FPGA.
read_write_example.c | Software application file written in C.
toggle_issp.tcl | Tcl script to toggle the internal reset register using In System Sources and Probes (ISSP).
top_21_4_0_67.qar | Quartus project archive file. Including Platform Designer system and top-level System Verilog file.

## Slide 21: Software Required for Nios V
  GNU RISC-V Embedded GCC
    https://github.com/xpack-dev-tools/riscv-none-embed-gcc-xpack/releases/tag/v8.3.0-2.3
    Download file: xpack-riscv-none-embed-gcc-8.3.0-2.3-win32-x64.zip
    Extract file in Quartus install directory
      C:\intelFPGA_pro\21.4\niosv
  CMake packages for binary distributes
    https://cmake.org/download/
    Download file: cmake-3.21.4-windows-x86_64.zip
    Extract file in Quartus install directory
      C:\intelFPGA_pro\21.4\niosv
  xPack Windows Build Tools
    https://github.com/xpack-dev-tools/windows-build-tools-xpack/releases/
    Download file: xpack-windows-build-tools-4.2.1-2-win32-x64.zip
    Extract file in Quartus install directory
      C:\intelFPGA_pro\21.4\niosv

## Slide 22: Software Required for Nios V

## Slide 23: Path Environment Variable for Nios V

## Slide 24: Verify Path Correctness

## Slide 25: Demo